## Slide 1: Chargeable-User-Identity
Scott Armitage

## Slide 2: Introduction
Scott Armitage
  Loughborough University
  eduroam UK Support

## Slide 3: What is CUI?
Chargeable-User-Identity (CUI)
  RFC4372
  Unique Identifier for an eduroam user
  Same across different devices
  Unique per visited site

## Slide 4: Why is CUI useful?
How many visitors do you have?
How do you block a single user?
Sites only have outer identity and calling station id
  User can change both of these

## Slide 5: eduroam Policy
eduroam UK Policy
  Sites should respond with CUI if requested
  Recommend sites should request CUI
  If CUI is received it must be logged
eduroam Service Policy
  Recommended sites return a CUI if requested
  Request must contain Operator Name
  Only home site should be able to reverse CUI

## Slide 6: How do I request a CUI?
Visitor at your site
  Request CUI by sending nul CUI ‘\\000’ in all request packets
  Must send Operator-Name

## Slide 7: How do I generate a CUI?
Received nul CUI attribute in Access-Request
  Ignore if Operator-Name is missing
  Md5 hash
    Operator-Name
    User-Name
    Salt
  Record CUI
  Reply with CUI value in all RADIUS packets

## Slide 8: Received a CUI
CUI should be recorded in logs
  e.g. syslog
NAS which support CUI should include the CUI in all Accounting Packets

## Slide 9: support.roaming.ja.net
Simulated visitor test supports CUI
Currently tests through support site don’t